## Slide 1
PREDICTION OF
ROCK PROPERTIES
Application of Machine Learning in predicting Mechanical Properties of Rocks

## Slide 2
ROCK PROPERTIES
  Density
  Porosity
  P-wave Velocity
  Point Load Strength Index
  Uniaxial Compressive Strength(UCS)
  Elasticity
  Brazilian Tensile Strength

## Slide 3
DENSITY
  Density of the Rock= Mass/Volume
  How is it Calculated:
  Measuring Mass:
Requires a Balance Scale
  Measuring Volume:
Can be found by Submersion

## Slide 4
POROSITY
  Porosity is a measure of the open space or voids within a rock or soil
  porosity= (%)=(Volume of Voids/ Total Rock Volume)×100
  How is it Calculated:
  Mercury Intrusion Porosimetry:
Mercury intrusion porosimetry is a laboratory technique used to measure the distribution of pore sizes in a rock sample. The method involves immersing the rock sample in mercury and applying pressure, which forces the mercury into the open pores. The intrusion volume at different pressure levels is then measured. By analyzing the relationship between pressure and intrusion volume, scientists can determine the size and distribution of pores, providing insights into the rock's porosity characteristics

## Slide 5
P-WAVE VELOCITY
  It is the speed at which compressional or primary seismic waves travel through a material, such as rocks
  P-wave velocity (Vp=d/t)​
  How is it Calculated: P-wave velocity in rock is determined by introducing P-waves into a rock sample using a seismic source, measuring the travel time with seismometers

## Slide 6
POINT LOAD INDEX
  The Point Load Strength Index (PLSI) is a measure used in geotechnical and rock mechanics to assess the strength of rock or geological formations.
  P load=2P/d
  How is it Calculated:
  The PLSI test involves applying a concentrated load to a rock specimen using a pointed tip. The load is applied parallel to the bedding plane or foliation of the rock. The test measures the point load strength, which is the force required to fracture the rock divided by the cross-sectional area of the rock specimen at the point of loading.

## Slide 7
UNIAXIAL COMPRESSIVE STRENGTH
UCS
  It represents the maximum stress that a cylindrical or cubical rock sample can sustain under a uniaxial (vertical) compressive load without failing
  UCS = Maximum Axial Load/Cross-sectional Area of the Rock Specimen
  How is it Calculated:
The UCS test involves preparing a cylindrical or cubical rock specimen with standardized dimensions. The specimen is then loaded axially in a hydraulic testing machine until failure occurs. The applied load and the dimensions of the specimen are used to calculate the UCS.

## Slide 8
ELASTICITY
  Elasticity, specifically Young's Modulus (E), is a measure of the stiffness or rigidity of a rock. It indicates the rock's ability to deform under stress and return to its original shape once the stress is removed.
  E = stress applied to the rock/ resulting strain (deformation)
  How is it Calculated:
, the stress is usually uniaxial compressive stress, and strain is the resulting axial strain.

## Slide 9
BRAZILIAN TENSILE STRENGTH
  The Brazilian Test is valuable for estimating the tensile strength of rocks, which is an essential parameter in understanding the overall mechanical behavior of rocks
  T_b = 2p/pi D
  How is it Calculated:
Brazilian Test, is a method used to determine the tensile strength of rocks. In this test, a cylindrical rock specimen is subjected to diametral loading, causing the rock to fail in tension along a diameter perpendicular to the loading direction.

## Slide 10
WHY MACHINE
LEARNING
  Data-driven Predictions
  Multivariable Analysis
  Improved Accuracy
  Pattern Recognition
  Uncertainty Estimation
  Cost Reduction
  Real-time Monitoring
  Time effectiveness
SVM
KNN
Linear Regression
RF
BPNN

## Slide 11
RESULTS
SVM

## Slide 12
RESULTS
BPNN

## Slide 13
RESULTS
RF(RANDOM FORESTS)

## Slide 14
RESULTS
LINEAR REGRESSION

## Slide 15
RESULTS
KNN

## Slide 16
ACCURACY
OVERALL
Our results demonstrated that the SVM-based model
shows a better performance than all the other models

## Slide 17
THANK YOU
112101010@smail.iitpkd.ac.in
112101012@smail.iitpkd.ac.in
Chapati Anusha, Chitturi Laasya Priya